## Slide 1: Title: Autonomous Robotic Scrap Sorting System
Team members:
AAKASH GS:CB.SC.U4AIE24101
VIGNESH:CB.SC.U4AIE24124
M.VISHNU TEJA:CB.SC.U4AIE24130
M.RAKESH:CB.SC.U4AIE24134

## Slide 2: INTRODUCTION
Core Concept: Autonomous hazardous waste management requires Perception + Decision + Safe Actuation.
Project Integration:
Perception: Camera-based object detection (OpenCV/ML).
Processing: Raspberry Pi 4 (Embedded Computing).
Manipulation: 3-DOF Robotic Arm with Electromagnetic End-Effector
Motivation: Manual segregation of sharp ferrous waste (scrap) is dangerous and inefficient. Vision-based classification improves safety and autonomy in robotic systems.

## Slide 3: PROBLEM STATEMENT
Current Issue: Manual sorting of hazardous waste (sharp metals, rusty iron) poses health risks to workers (tetanus, cuts).
Limitation: Simple blind robots cannot distinguish between valuable ferrous scrap and general waste.
Proposed Solution: A vision-driven robotic system that:
  Identifies ferrous objects using Computer Vision.
  Locates their precise coordinates (x, y, z).
  Segregates them safely using contactless magnetic lifting.

## Slide 4: Objective Of The Project
Design a Vision-Based Object Detection System to identify metal scrap.
Integrate Raspberry Pi control with PCA9685 for precise servo actuation.
Implement Inverse Kinematics (IK) for autonomous positioning.
Achieve Contactless Pick-and-Place using an electromagnetic end-effector.
Build a robust Hardware Proof-of-Concept using a 3-DOF manipulator.

## Slide 5: Mapping Objectives to the Course Scope
AIR Concept | Project Implementation
Serial Manipulators | 3-DOF Acrylic Robotic Arm (Base, Shoulder, Elbow, Wrist)
Inverse Kinematics | Geometric approach for computing Joint Angles (theta1, theta2, theta3)
Robot Control | I2C-based PWM control via PCA9685 Driver
Perception | Camera-based Object Detection & Coordinate Mapping
Hardware Integration | Raspberry Pi 5 + Buck Converter + Relay Logic

## Slide 6: Week wise Split-up Plan to Achieve Objectives
Week 1-2: Hardware procurement and mechanical assembly of the acrylic arm.
Week 3: Electrical wiring (Power distribution, Buck Converter tuning, Sensor integration).
Week 4: Python implementation of Forward Kinematics to visualize the arm's reach.
Week 5: Deriving and coding the Inverse Kinematics equations.
Week 6: Integrating the Camera and OpenCV for object detection.
Week 7: System integration (Vision to IK to Motor movement) and testing.
Week 8: Final optimization and Report writing

## Slide 7: SYSTEM ARCHITECTURE
System Components:
Fixed Overhead Camera: Raspberry Pi Camera / USB Webcam.
Central Processor: Raspberry Pi 5 (Vision Processing & Kinematics).
Motor Interface: PCA9685 16-Channel Servo Driver.
Actuation: 1xSG90 and 3xMG90S.
End-Effector: 12V DC Electromagnet (Controlled via Relay).
Information Flow:
Camera  Pi: Image Capture & Coordinate Extraction.
Pi  PCA9685: Joint Angle Commands (I2C).
Pi  Relay: Magnet ON/OFF Signal (GPIO).

## Slide 8: INVERSE KINEMATICS APPROACH
Robotic Arm Structure:
  1 Base Motor (Yaw - theta1)
  3 Arm Motors (Pitch - theta2, theta3,theta4)
Inverse Kinematics Computes:
  Required servo angles to reach the target (x, y, z) detected by the camera.
  Ensures the electromagnet lands flat on the scrap metal.
  Prevents mechanical singularities and collisions.

## Slide 9: VISION & DETECTION STRATEGY
Monitoring:
Overhead camera continuously monitors the workspace.
Detection Logic:
Captures frames in real-time.
Applies Color/Contour Detection (or ML Model) to find metal objects.
Data Extraction:
Identifies Object Center (u, v) in pixels.
Maps pixels to Real-World Coordinates (x, y) using a calibration factor.
Sends coordinates to the Kinematics Engine.

## Slide 10: Methodology
Forward Kinematics (FK):
We use FK to calculate the exact position (x, y, z) of the Electromagnet if we know the current angles of the motors. By using Denavit-Hartenberg parameters, we multiply the transformation matrices of each link to find the end-effector's pose. This helps us ensure the robot stays within its safe workspace.
Inverse Kinematics (IK):
This is our control strategy. Since the camera gives us the location of the scrap (x, y, z), we need to calculate what angles the motors need to turn to reach that spot. We are using a Geometric Approach (using trigonometry/cosine rule) rather than a numerical one, as it is faster for the Raspberry Pi to compute in real-time.

## Slide 11: METHODOLOGY
Image Capture: Capture real-time video of the workspace using the Pi Camera.
Preprocessing: Convert RGB images to Grayscale/HSV for efficient processing.
Object Detection: Identify ferrous scrap contours using OpenCV techniques.
Coordinate Mapping: Convert pixel centroid (u, v) to physical target coordinates (x, y, z).
Path Planning: Calculate joint angles using Inverse Kinematics.
Execution: Move arm to target  Activate Magnet  Transport to Bin.

## Slide 12: METHODOLOGY
Base Angle (theta1):
Reach Distance (r):
Elbow Angle (theta3) - Cosine Rule:
Shoulder Angle (theta2):
(Where L2, L3 are link lengths of the arm)

## Slide 13: EXECUTION LOGIC
Verify Position: Use Forward Kinematics (FK) to ensure target is within workspace limits.
Transmit: Send calculated angles to PCA9685 via I2C bus.
Drive: Servos move to the "Pick" position.
Actuate: Trigger Relay (GPIO 17 HIGH) to energize Electromagnet.
Transport: Move to "Drop" coordinates.
Release: Trigger Relay (GPIO 17 LOW) to drop scrap.

## Slide 14: HARDWARE IMPLEMENTATION
Processing Unit: Raspberry Pi 5 Model B (8GB).
Power Management:
Source: 12V 2A DC Adapter.
Regulation: LM2596 Buck Converter (12V  6V for Servos).
Isolation: 5V Relay Module for Magnet.
Actuators: 1xSG90 and 3xMG90S.
Integration: Successful wiring of I2C Drivers, GPIO Relay, and Camera module.

## Slide 15: Results & Discussion
Completed Work:
  Mechanical assembly of 3-DOF Acrylic Arm.
  Power distribution system (Buck Converter & Relay wiring) validated.
  Raspberry Pi OS setup and library installation (Adafruit Servokit).
  Basic servo motion tests (Sweep) successful.
Work in Progress:
  Integration of OpenCV for live object detection.
  Calibration of Inverse Kinematics for precise reaching.
  Final "Pick-and-Place" automation cycle testing.

## Slide 16: References
Rao, A. S., et al. (2017). "Web-Based Control of Robotic Arm Using Raspberry Pi." IEEE International Conference on Power, Control, Signals and Instrumentation Engineering.
Subha, T. D., et al. (2017). "Automatic Waste Segregator and Monitoring System." International Research Journal of Engineering and Technology (IRJET).
Levine, S., et al. (2018). "Learning Hand-Eye Coordination for Robotic Grasping with Deep Learning." The International Journal of Robotics Research.

## Slide 17
THANK YOU